| Drawings Reviewed: (titles plus dates): | Project Name: Project Number: Review By: Date: Approved By: BCDN: |
| --- | --- |

Legend: N Not required R Required C Confirm requirements or RC Review completed and item construction detail(s) indicated on documents This checklist is intended to assist architects in a review of code requirements to be considered in the preparation and review of documents to support a permit application. A simple review of the checklist is not a substitute for a thorough review of the OBC. Modify the checklist to note applicable code requirements for the project.

1. BUILDING HEIGHT AND AREA 	                                                                                                                                             OBC Code Reference(s)

|  | a | Storeys above grade and building area | 2.1.1.3 |
| --- | --- | --- | --- |
|  | b | Room and space dimensions | 9.5 |
|  | c | Shoring details | 9.12.1.4 |

2. FIRE SAFETY PROTECTION

|  | a | % of unprotected openings (>130cm2) | 9.10.14.1 to 9.10.14.10 |
| --- | --- | --- | --- |
|  | b | F.R.R. of external wall and construction non-combustible cladding where LD<600mm” | 9.10.14.11 & 9.10.14.12 |
|  | c | F.R.R. of external wall and construction, dwelling above another | 9.10.14.11 |
|  | d | Protected openings | 9.10.14.5 |
|  | e | Rating for closures | 9.10.13.1 |
|  | f | Party walls (see S.P. for wood party walls) | 9.10.11.2., 9.10.11.4 & 9.11.2 |
|  | g | Firewalls (internal, external req’ts) | 9.10.11 & 9.11.2 |
|  | h | Combustible projection in townhouse | 9.10.14.13 |
|  | i | Protection of soffits (common attic > 2 suites) | 9.10.12.5 |
|  | j | Fire stopping | 9.10.15 |
|  | k | Gas proofing of garage | 9.10.9.16.(3) |
|  | l | Garage floor slope | 9.35.2.2 |
|  | m | Doors from garage | 9.10.13.15 & 9.6.5.6 |
|  | n | Single exit travel >1 storey: provide balcony (or window when no dwelling above another) | 9.9.9 |
|  | o | Forced entry requirements | 9.6.8. & 9.7.6 |
|  | p | Openable window each level with bedrooms (0.35m2/380mm clear opening max.) | 9.7.1.3 & 9.7.1.4 |
|  | q | Windows or access panels (when dwelling above another) | 9.10.19.1 |
|  | r | Smoke alarms on each floor level (interconnected) | Carbon monoxide detector | 9.10.18 & 9.33.4 |

3. FOOTINGS AND FOUNDATIONS

|  | a | Soil bearing capacity (minimum 75 KPA) | 9.4.4.1 & Table 9.4.4.1 |
| --- | --- | --- | --- |
|  | b | Size of footings/ basement column pad footings | bb SG-10 for joists > 4.9 m/16’ span | 9.15.3.3., Table 9.15.3.3, SG-10 |
|  | c | Frost coverage | 9.12.2.2. & Table 9.12.2.2 |
|  | d | Max. foundation wall height (watch for laterally unsupported walls at stair opening/framing) | 9.15.4.1 & Table 9.15.4.1 |
|  | e | Height above grade min 150 mm | 9.15.4.3 |
|  | f | Reduced thickness | 9.15.4.4.(1) to (3) |
|  | g | Capping & parging (concrete block only) | 9.15.5.1, 9.15.6.1 & 9.15.6.2 |
|  | h | Dampproofing & drainage layer | 9.13.3, 9.14.2 |
|  | i | Drainage and coverage | 9.14.3. & 9.14.4.2 |
|  | j | Step footings | 9.15.3.8 |
|  | k | Sill plate anchorage & levelling | 9.23.7.2 & 9.23.6.1 & 9.23.6.2 |

4. CONCRETE SLABS

|  | a | Concrete strength | 9.3.1.6 & 9.3.1.7 |
| --- | --- | --- | --- |
|  | b | Reinforcement for structural slabs | 9.3.1.9 & Part 4 |
|  | c | Basement floor drain | 9.31.4.4 |

5. STRUCTURAL COMPONENTS

|  | a | Max. deflections | Table 9.4.3.1 |
| --- | --- | --- | --- |
|  | b | Lintels for masonry | Tables 9.20.5.2.A & 9.20.5.2.B |
|  | c | Wood dintels | 9.23.12.3 & Tables A-13 to 20 |

|  | d | Steel beams supporting floors (calculation by P.Eng Yes/No) |  | Table 9.23.4.3 & Part 4 |
| --- | --- | --- | --- | --- |
|  | e | Joists and steel beams | 9.23.9.2.(1) to (5) |
|  | f | Steel columns | 9.17.3.1 to 9.17.3.4 |
|  | g | Wood columns | 9.17.4.1 to 9.17.4.4 |
|  | h | Masonry/concrete columns | 9.17.5 & 9.17.6 |

6. FLOOR CONSTRUCTION

|  | a | Floor joists and beams (proprietary joist manufacturer Yes/No) |  | 9.23.4.1 & Tables A-1 to A-11 |
| --- | --- | --- | --- | --- |
|  | b | Strapping & bridging (engineered IBS bridging Yes/No) |  | 9.23.9.4 & Tables A-1 & A-2 |
|  | c | Cantilevered floor joists | 9.23.9.10 & Table 9.23.3.4 |
|  | d | Concrete topping | 9.23.4.4 & Tables A-1, A-8,,A-11 |

7. WOOD FRAME WALLS

|  | a | Stud size/spacing (2 floors-38x89 @ 300o/c) | 9.23.10 & Table 9.23.10.1 |
| --- | --- | --- | --- |

8. MASONRY/STONE VENEER

|  | a | Thickness & height | 9.20.1.1., 9.20.6.4 |
| --- | --- | --- | --- |
|  | b | Veneer ties | 9.20.9.5 & Table 9.20.9.5 |
|  | c | Sheathing paper | 9.23.17.1 to 9.23.17.3 |
|  | d | Control of rain water penetration | 9.20.13.1 to 9.20.13.8 |

9. ROOF AND CEILING CONSTRUCTION

|  | a | Ceiling joists | 9.23.4.1, Table A-3, 9.23.13.10 |
| --- | --- | --- | --- |
|  | b | Roof joists | 9.23.13.9 Tables A-4, A-5 |
|  | c | Roof rafters max. 9.75 m (32’0”) | 9.23.13.8, Tables A-6, A-7 |
|  | d | Additional roof loads (clay tile) | 9.23.4.5 |
|  | e | Roof trusses (check layout, beams req’d bearing P.Eng. stamp - attach layout and girder truss to drawing) | 9.23.13.11.(1) to (6) |
|  | f | Collar ties | 9.23.13.7.(1) & (2) |

|  | g | Struts, dwarf walls | 9.23.13.7.(3) to (5) |
| --- | --- | --- | --- |
|  | h | Ridge support (slope <4:12 or no wall ties) | 9.23.13.8.(1) & (2) |
|  | i | Wall ties | 9.23.13.8.(4) |

10.	ROOF DETAILS

|  | a | Roof space ventilation(1:150; 1:300; mansard & soffitless roofs) | 9.19.1.1 to 9.19.1.4 |
| --- | --- | --- | --- |
|  | b | Cathedral ceilings | 9.19.1.2. & 9.19.1.3 |
|  | c | Slope | 9.26.3.1 Table 9.26.3.1 |

11.	INSULATION

|  | a | Areas to be insulated and amount required | Table 9.25.2.1(Zone 1) |
| --- | --- | --- | --- |
|  | b | Thermal design: by Arch. or P.Eng. | 9.38 |
|  | c | Eave protection | 9.26.5.1.(1) & .(2) |
|  | d | Air & vapour barriers | 9.25.3; 9.25.4 |

12.	NATURAL LIGHT & VENTILATION

|  | a | Finished rooms, interior rooms, laundry | Table 9.7.1.2 & 9.32.1.2 & 9.32.2 |
| --- | --- | --- | --- |

13.	STAIRS

|  | a | Interior & exterior stairs | 9.8.3.1.(1) & (2) & 9.8.3.2 |
| --- | --- | --- | --- |
|  | b | Width & headroom | 9.8.3.3 & 9.8.3.4. |
|  | c | Curved stairs and winders | 9.8.5. |
|  | d | Landings (check if rear deck required) | 9.8.4. |
|  | e | Handrails | 9.8.7. |
|  | f | Foundation required | 9.8.9.1. |

14.	GUARDS

|  | a | Interior & exterior stairs | 9.8.8.2.(4) & (5) |
| --- | --- | --- | --- |
|  | b | Balcony, stairwells, porches, landings | 9.8.8.2.(1) to (5) |
|  | c | Construction (P.Eng. design or SG-7 details) | 9.8.8.4 to 9.8.8.8 & SG-7 |

15. CHIMNEYS

|  | a | 650oC chimney (ULC S629) | 9.21.1.2 |
| --- | --- | --- | --- |
|  | b | Chimney flues serve fireplace only | 9.21.2.1 |
|  | c | More than one applicance | 9.21.2.2 |
|  | d | Inclined 45o max to the vertical | 9.21.2.3 |
|  | e | Clearance to combustibles | 9.21.5.1 |
|  | f | Chimney flue clearance to joists, beams | 9.21.5.3 |

16.	SOLID FUEL – APPLIANCES

|  | a | Masonry fireplaces (wall thickness)(check framing around fireplaces & chimneys) | 9.22.1.2 |
| --- | --- | --- | --- |
|  | b | Fireplace liner (steel liners – ULC S639M) | 9.22.2 |
|  | c | Hearth, damper & smoke chamber | 9.22.5, 9.22.6, 9.22.7 |
|  | d | Prefab fireplaces (ULC S610) | 9.22.8.1, 9.33.1.2 |
|  | e | Clearance to combustibles (from smoke chamber25mm (1”) | 9.22.9 |
|  | f | Combustion air requirement; HRV (co-ordinate with mech.) | 9.22.1.4.(1) to (7), 9.32.3.8 |
|  | g | Fireplace inserts (ULC S628 &CSA B365M) | 9.22.10 |
|  | h | Stoves (ULC S627 & CSA B365M) | 9.33.1.2 |